# Text boxes

C & D

TENT ERECTION INSTRUCTIONS

###### FLYSHEET FIRST PITCHING

- Assemble poles and lay them on the ground parallel: (8 poles: 2 longer (thicker) diagonal poles (A) (B) 6 slightly shorter (slimmer) poles equal length (C) (D) (E) (F) (G) & (H)			     Note: All poles are colour coded to match colour coding on pole sleeves.

- Open out flysheet and position side and end doorways in required direction.

- Insert the two larger diagonal poles through the pole sleeves running across the centre of the flysheet (leave loose)  (A) (B)

- Insert the six slimmer poles through the pole sleeves running across the width of the flysheet.  (Two each side of diagonal poles) (C) (D) (E) (F) and 2 at rear of tent (G) & (H).

- Locate one end of each pole on one side of flysheet into the metal pin at the end of the pole sleeve.  Make sure poles locate into correct anchor tapes (all poles follow flysheet seams to anchor straps).

- Push diagonal poles into an arch from opposite ends and locate pole ends into corresponding metal pin. (To avoid excess strain on poles and tent material, it is advisable to have assistance to hold diagonal poles upright when forming arch).

- Push remaining six poles into an arch and locate pole ends into corresponding metal pin.

- Peg out one end of flysheet by means of anchor straps at each corner.

- Pull flysheet from opposite end until tent is fully extended and flysheet is taut.  Peg down anchor straps at each corner.

- Peg down remaining pegging points on flysheet, attach guylines and peg down.

A & B

## CATALAN 7200

###### INNER TENT/S

- Open out inner tent/s inside flysheet and position groundsheet to match flysheet (with inner tent doors facing centre of tent).

- Attach elasticated plastic clips on rear of groundsheet to corresponding plastic rings on flysheet anchor straps.

- Suspend rear of inner tent to inside of flysheet by attaching elasticated toggles through corresponding eyelets on side of flysheet.

- Attach elasticated plastic clips on front of groundsheet to corresponding plastic rings on pole anchor straps.

- Suspend front of inner tent to inside of flysheet by attaching elasticated toggles through corresponding eyelets on side of flysheet.

- Repeat procedure for attaching other inner tent (if required).

- Open out and peg down separate groundsheet between the inners.

G & H

E & F